## Slide 1
Generalized sensitivity functions for optimal b-value selection in diffusion-based MRI modeling
Umberto Villani1,2, Simona Schiavi3, , Alessandra Bertoldo1,2
1Padova Neuroscience Center, University of Padova, Italy, 2Department of Information Engineering, University of Padova, Italy, 3Computer Science department, University of Verona, Italy
email: umberto.villani@phd.unipd.it
BACKGROUND
METHODS
CONCLUSIONS
Optimal experiment design criteria (1) are nowadays widely used in biological modelling to assess which possible empirical observations yield the most information regarding specific model parameters.
Generalized sensitivity functions (GSFs) (2) provide a mean for studying how the employed models effectively respond to different experimental conditions, by additionally employing some a priori knowledge about noise fluctuations affecting the measurements.
These procedures can be
computationally tedious
Risk of yielding magic numbers!
What happens in the neighborhood
of those values?
In the present study, we wish to reformulate the GSF context in the diffusion MRI field in order to understand which
b-values play a central role for accurate model identification.
The sensitivity analysis we propose normalizes the Fisher information computed on a subset of q-space observations (for the case and models at hand, we refer to diffusion shells with diffusion time and pulse duration fixed) over the Fisher information defined across a comprehensive range of defined b-values. We refer to the generalized sensitivity matrix as
Where is the length of the b-value vector , and is the shell-wise Fisher Information matrix, whose exact formulation depends on the biophysical model and the noise probability density function. For the most common gaussian case, becomes (3)
where is the set containing all the diffusion gradient directions, denotes the gradient operator with respect to the model parameters and is the studied biophysical model prediction. The generalized sensitivity functions for the model parameters are then extracted from the GS matrix in [1]:
As GSFs are cumulative functions, the most informative shells are associated with the steepest increase of their trajectories (2).
We demonstrate the usefulness of GSFs by displaying them for the following diffusion approaches and specific choice of estimators (4-6): Diffusion Tensor Imaging (Linear Least Squares), Diffusion Kurtosis Imaging (Non-Linear Least Squares) and Neurite Orientation Dispersion and Density Imaging (Rician Maximum likelihood).
REFERENCES
(1) Herzberg et al., Biometrika, 1972; (2) Thomaseth et al., Ann Biomed Eng, 1999; (3) Seber et al., 1989; (4) Basser et al., Biophys J., 1994; (5) Jensen et al., Magn Reson Med, 2005; (6) Zhang et al., Neuroimage, 2012., (7) Van Essen et al., Neuroimage, 2013.
Diffusion Tensor Imaging (DTI)
While the single tensorial components have slightly different curves, their general behaviour is the same, exhibiting the steepest increase (and thus, the most information gain) in the interval from 1000 to 2500 s/mm2, value for which the curves are starting to plateau.
Diffusion Kurtosis Imaging (DKI)
We can see different patterns in this case. The first one is similar to the GSFs in Figure 1, and it is followed by the six parameters representing the kurtosis-corrected diffusion tensor, with an optimal range of b-values around 1000-1500 s/mm2 ; the second one belongs to the Kurtosis Tensor components, for which the information gain starts from b=2500 s/mm2 onwards. Thus, the present method effectively suggests the necessity of two b-shells in order to accurately estimate all DKI parameters.
Neurite Orientation Dispersion and Density Imaging (NODDI)
The isotropic volume estimation highly benefits from a shell in the 200-900 s/mm2 range, while the intracellular volume features a pronounced information gain with a shell from b=1500 s/mm2 onwards: these findings agree with the proposed optimized NODDI protocol (6). Interestingly, we find the Watson concentration parameter (conveying the information of the Orientation Dispersion Index) has no optimal ranges for its estimation and draws its precision homogeneously across the studied b-value space.
The issue of parametrical correlations
Both the DKI and NODDI GSFs feature severe overshoots/undershoots from the expected value range [0-1]. These issues are present when the non-diagonal elements of are significantly large, which in turn are caused by large correlations amongst different parameters (3).
The present work introduces generalized sensitivity functions and demonstrate their use for visually exploring which ranges of b-values are most informative for model parameters when defining HARDI acquisition protocols. GSFs are not meant to substitute optimal experiment design procedures, but can rather provide characterizing information for proper contextualization of their results. They are computationally light to generate and employ information easily derivable by standard fitting routines, supporting their inclusion in standard modeling analyses.
DATASET
We used a single healthy subject from the publicly available Human Connectome Project (7) to fit the aforementioned models. We then took a representative voxel for the Corpus Callosum and used the parameter estimates to generate the GSFs.
Diffusion protocol: A subset of the HCP diffusion acquisition: 10 B0 images, 64 isotropically dispersed gradient directions at both b1=1000 s/mm2 and b2=3000 s/mm2
Preprocessing: The diffusion images underwent the minimal HCP preprocessing pipeline, featuring gradient nonlinearity, motion and eddy currents corrections.
RESULTS